| Мутимедиен проектор | - 5 броя |
| --- | --- |
| Естествена разделителна способност | 800 x 600 (SVGA) |
| Яркост | 2700 ANSI lumens |
| Съотношение на контраст | 13000:1 |
| Обектив | F=2.56-2.8, f=21-23.1mm |
| Аспектно съотношение | Native 4:3 (5 aspect ratio selectable) |
| Фокусно съотношение | 1.86 - 2.04 (53”@2m) |
| Размер на изображението (по диагонал) | 40”-300” |
| Съотношение на увеличаване | 1.1:1 |
| Лампа (нормален/икономичен режим/режим SmartEco) | 4500/6000/6500 hours |
| Корекция на трапецовидното изкривяване | 1D, Vertical +/- 40 degrees |
| Прожекционно отместване | 120% |
| Поддръжка на разделителна способност | VGA(640 x 480) to UXGA(1600 x 1200) |
| Честота на хоризонтална разгъвка | 31K~102KHz |
| Вертикална честота на сканиране | 23~120Hz |
| Интерфейс | Computer in (D-sub 15pin) x 2(shared with Component) |
|  | Monitor out (D-sub 15pin) x 1 |
|  | Composite Video in (RCA) x 1 |
|  | S-Video in (Mini DIN 4pin) x 1 |
|  | Audio in (Mini Jack) x 1 |
|  | Audio out (Mini Jack) x 1 |
|  | Speaker 2W x 1 |
|  | USB (Type Mini B) x 1 |
|  | RS232 (DB-9pin) x 1 |
| Съвместимост с HDTV | 480i, 480p, 576i, 576p, 720p, 1080i, 1080p |
| Видео съвместимост | NTSC, PAL, SECAM |
| Доловим шум | 33/26 dBA (Normal/Economic mode) |
| 3D Support and Compatibility | PC: 120Hz Frame Sequential 3D for resolutions up to WXGA |

| Мини проектор | 2 броя |
| --- | --- |
| Яркост: | 15лумена |
| Технология на дисплея: | LCOS(3M) |
| Разделителна способност: | 640 х 480 |
| Съотношение: | 04:03 |
| Контраст: | 200:01:00 |
| Фото: | JPEG, BMP, GIF |
| Аудио: | MP3,WMA,WAV,APE,FLAV,AAC,AC3,OGG |
| Видео: | MPEG4,AVI,RM,RMVB,FLV,WMV,3PG,MP4,MKV,MAC |
| Входове: | VGA вход, AV вход, USB вход, YPbPr/YCbPr вход, |
| Памет | Вградена 2 GB памет, поддържа микро SD карта. |
| Фокус режим: | Ръчен фокус, проектира размера 6"-150" |
| Говорител: | 1 х 1W |
| Захранване: | 5V/3A, вградена 1700mAh литиева батерия |

| Мутимедиен проектор | - 12 броя |
| --- | --- |
| Естествена разделителна способност | 1024 x 768 (XGA) |
| Яркост | 2700 ANSI lumens |
| Съотношение на контраст | 13000:1 |
| Обектив | F=2.56-2.8, f=21-23.1mm |
| Аспектно съотношение | Native 4:3 (5 aspect ratio selectable) |
| Фокусно съотношение | 1.86 - 2.04 (53”@2m) |
| Размер на изображението (по диагонал) | 40”-300” |
| Съотношение на увеличаване | 1.1:1 |
| Лампа (нормален/икономичен режим/режим SmartEco) | 4500/6000/6500 hours |
| Корекция на трапецовидното изкривяване | 1D, Vertical +/- 40 degrees |
| Прожекционно отместване | 120% |
| Поддръжка на разделителна способност | VGA(640 x 480) to UXGA(1600 x 1200) |
| Честота на хоризонтална разгъвка | 31K~102KHz |
| Вертикална честота на сканиране | 23~120Hz |
| Интерфейс | Computer in (D-sub 15pin) x 2(shared with Component) |
|  | Monitor out (D-sub 15pin) x 1 |
|  | Composite Video in (RCA) x 1 |
|  | S-Video in (Mini DIN 4pin) x 1 |
|  | Audio in (Mini Jack) x 1 |
|  | Audio out (Mini Jack) x 1 |
|  | Speaker 2W x 1 |
|  | USB (Type Mini B) x 1 |
|  | RS232 (DB-9pin) x 1 |
| Съвместимост с HDTV | 480i, 480p, 576i, 576p, 720p, 1080i, 1080p |
| Видео съвместимост | NTSC, PAL, SECAM |
| Тегло | 2.4 kg. |
| Доловим шум | 30/26 dBA (Normal/Economic mode) |
| Захранване | AC 100 to 240 V, 50/60 Hz |
| Консумация на енергия | 275W, Standby<0.5W |
| 3-измерна поддръжка и съвместимост | PC: 120Hz Frame Sequential 3D for resolutions up to WXGA |

| Мутимедиен проектор | - 3 броя |
| --- | --- |
| Естествена разделителна способност | 1280 x 800 (WXGA) |
| Аспектно съотношение | 16:10 |
| Яркост | 2600 ANSI Lumen (approx. 75% in Eco Mode ) |
| Съотношение на контраст | 2000:1 |
| Лампа (нормален/Eco) | 4000 (5000 Eco Mode ) |
| Ъгъл на проектиране [°] | 37.3 - 38.6 |
| Разстояние на проектиране[m] | 0.6 – 1.1 |
| Размер на изображението (по диагонал) [cm] | Minimum: 142.2 / 56"; Maximum: 264.2 / 104" |
| Поддръжка на разделителна способност | 1920 x 1080 (HDTV 1080i/60; HDTV 1080i/50); 1680 x 1050 (WSXGA+); 1600 x 1200 (UXGA); 1600 x 900 (WXGA++); 1440 x 900 (WXGA+); 1400 x 1050 (SXGA+); 1366 x 768 (WXGA); 1360 x 768 (WXGA); 1280 x 1024 (Maximum resolution of digital input); 1280 x 1024 (SXGA); 1280 x 1024 (SXGA); 1280 x 1024 (MAC 23"); 1280 x 960 (SXGA); 1280 x 800 (WXGA); 1280 x 768 (WXGA); 1280 x 720 (HDTV 720p); 1152 x 870 (MAC 21"); 1152 x 864 (XGA); 1024 x 768 (XGA); 832 x 624 (MAC 16"); 800 x 600 (SVGA); 720 x 576 SDTV 576p/576i; 720 x 576 (DVD progressive); 720 x 480 SDTV 480p/480i; 720 x 480 (SDTV 480p); 640 x 480 (VGA/MAC 13") |
| Честота на хоризонтална разгъвка | Horizontal: 15–100 kHz (RGB: 24 kHz– 100 kHz) |
| Вертикална честота на сканиране | Vertical: 50 – 120 Hz |
| Интерфейс | Input: 2 x Mini D-sub 15-pin, compatible to component (YPbPr) Input: 1 x HDMI™ (Deep Color, Lip sync) Input: 1 x RCA Input: 1 x Mini DIN 4-pin Input: 2 x 3.5 mm Stereo Mini Jack; 2 x RCA Stereo Input: 1 x D-Sub 9 pin (RS-232) (male) LAN RJ45 USB Type B; 2 x Type A (USB 2.0 high speed) Output: 1 x 3.5 mm Stereo Mini Jack (variable) |
| Видео сигнал | PAL; PAL60; NTSC; SECAM; NTSC 4.43; PAL-M |
| Тегло | 2.4 kg. |
| Доловим шум [dB (A)] | 29 / 35 (Eco / Normal) |
| Високо говорители | 1 x 10 W (mono) |

| Стойка за късофокусен мултимедиен проектор | - 3 броя |
| --- | --- |

| Интерактивна дъска | - 3 броя |
| --- | --- |
| Активна област: | 96” (2446 mm) diagonal |
| Аспектно съотношение: | 16:09 |
| Технология | IR (Infrared) cell LED optical |
| Разделителна способност | 12800x9600 |
| Board size without packing: | 2269 x1249x30 mm (width x height x depth without plastic pen tray) |
| Интерфейс | USB 2.0 / 2.4 GHz RF Wireless (optional) |
| Време на реакция | 6ms |
| Захранване | USB DC 5V from PC (optional wireless PC receiver and USB adaptor /220V) |
| Поддържани ОС | Windows 7, Linux, MAC |
| Тегло | 28 kg |

| Безжичен адаптер за Интерактивна дъска | - 3 броя |
| --- | --- |

| Скенер | - 3 броя |
| --- | --- |
| Тип | Flatbed |
| Оптична разделителна способност | Up to 4800 dpi |
| Цвят | 48-bit |
| Адаптер за филми | Built-in (TMA); four 35 mm slides or five 35 mm negative frames |
| Скорост на работа | 10 x 15 cm colour photo to file: about 9 sec for multiple image scan, up to 28 sec for single image scan |
| Scan size (flatbed), maximum | 216 x 297 mm |
| Типове медия | Paper (inkjet, laser, plain), photographic material (silver halide, pigment-dye), 3-D objects, 35 mm slides and negatives (using transparent media adapter) |
| Скорост на предварителен преглед | 11 sec |
| Контролен панел | 4 buttons (Copy, Scan, Scan to E-mail, Scan to PDF) |
| Интерфейс | Hi-Speed USB 2.0 |
| Консумация | 15 watts maximum |
| ENERGY STAR® | Yes |
| Тегло | 2.9 kg |

| Лазерен Принтер | - 9 броя |
| --- | --- |
| Скорост на печат | up to 20 ppm |
| Месечно натоварване | Up to 30,000 images/month |
| Време за печат на първа страница | As fast as 8 seconds |
| Разделителна способност | 1200 x 1200 dpi |
| Процесор | 150 MHz |
| Вградена памет | 64 MB |
| Интерфейс | USB 2.0 |
| Капацитет за хартия | Tray (Main tray): 150 sheets |
| Типове хартия | Tray (Main tray): Cover, Envelopes, Labels, Plain paper, Recycled paper |
| Размер на хартията | Tray (Main tray): Custom sizes: 76 x 127 mm to 216 x 356 mm |

| Лазерен Принтер | 5 броя |
| --- | --- |
| Резолюция | 1200 x 1200 dpi |
| Скорост | 33 ppm |
| Време за печат на първа страница | As fast as 8 seconds |
| Вградена памет | 256 MB |
| Интерфейс | 1 Hi-Speed USB 2.0; 1 Host USB; 1 Walk-up USB |
| Мрежа | 1 Ethernet 10/100/1000 Base-TX network |
| Медия, тип | Paper (plain, Green mode, light, heavy, bond, colour, letterhead, preprinted, prepunched, recycled, rough); envelopes; labels; transparencies, cardstock |
| Медия, размер | Tray 1: A4; A5; A6; B5 (JIS); envelopes; 76 x 127 to 216 x 356 mm; Tray 2: A4; A5; A6; B5 (JIS); 105 x 148 to 216 x 356 mm; Tray 3 (optional): A4; A5; A6; B5 (JIS); 105 x 148 to 216 x 356 mm |
| Медия, g/m2 | Tray 1: 60 to 163 g/m2 (straight through paper path for special media); Tray 2: 60 to 120 g/m2; Tray 3 (optional): 60 to 120 g/m2 |
| Капацитет за хартия - Входяща тава | Tray 1: 50 sheets; 10 envelopes; Tray 2: 250 sheets; Tray 3 (optional): 500 sheets |
| Капацитет за хартия - Изходяща тава | Up to 150 sheets; Up to 10 envelopes |
| Двустранен печат | Automatic (standard) |
| Натоварване, стр./месец | Up to 50 000 pages (monthly, A4); Recommended Monthly Page Volume: 750 to 3000 pages |

| Преносим компютър | 2 броя |
| --- | --- |
| Процесор | Intel Celeron B820 (1.70 GHz, 2MB L3 cache) |
| Системна памет | 3GB DDR3 |
| Твърд диск | 500GB SATA (5400 оборота/минута) |
| DVD Super Multi устройство | да |
| Дисплей | 15.6-инчов (39.62 см.) - 1366x768, матов |
| Интерфейси | 3x USB 2.0 |
|  | вгардена уеб камера |
|  | вграден микрофон |
|  | вход за микрофон |
|  | HDMI изход |
|  | VGA (аналогов ) |
|  | изход за слушалки и тонколони |
|  | вход за мрежови кабел |
|  | 4 в 1 четец за карти памет |
| Свързаност | LAN 10/100/1000 Мбит/сек, Wi-Fi 802.11 b/g/n, Bluetooth 4.0 |
| Тегло | 2.30 кг |
| Батерия | 6-клетъчна батерия (48 Wh) |

| Преносим компютър | 10 броя |
| --- | --- |
| Процесор | Процесор Intel® Pentium® B960 2.20 GHz |
| Цвят на дизайна | Бяло перлено покритие |
| Системна памет | стандартна : 4,096 МБ |
|  | максимална разширяемост : 8,192 МБ |
|  | DDR3 RAM (1 333 MHz) |
| Твърд диск | капацитет : 640 ГБ |
|  | скорост на въртене на устройството : 5,400 об./мин. |
| DVD Super Multi устройство | да |
| Дисплей | размер : 39,6 см (15,6”) |
|  | тип : 16:9 и светодиодна подсветка |
| Графичен адаптер | тип : Графична карта AMD Radeon™ HD 7610M (специализирана памет 1 ГБ) |
| Вътрешни видео режими | вътрешни видео режими: |
|  | разделителна способност : 1366 x 768 |
| Макс. външни видео режими | макс. разделителна способност : 2048 x 1536 макс. скорост на опресняване : 100 Хц последователна разделителна способност с макс. скорост на обновяване : 1600 x 1200 |
| Интерфейси | 1 × външен монитор |
|  | 1 × RJ-45 |
|  | 1 × външен микрофон |
|  | 1 × слушалки (стерео) |
|  | 2 × USB 2,0 |
|  | 1 × Четец на карти (поддържа SD™ карти до 2 ГБ, miniSD™/microSD™ карти с адаптер до 2 ГБ, SDHC™ карти до 32 ГБ, SDXC™ карти до 64 ГБ и MultiMedia Card™ до 2 ГБ) |
|  | 1 × HDMI изход, поддържащ формат на сигнала 1080p |
|  | 1 × интегрирана 1-мегапикселова HD уеб камера (1280 x 800) с вграден микрофон |
|  | 1 × USB 3.0 |
| Безжична комуникация | Съвместимост : Wi-Fi® Мрежова поддръжка : 802.11b/g/n |
| Кабелна комуникация | Fast Ethernet LAN |
| Звукова система | поддържан аудио формат : 24-битово стерео високоговорители : вградени стерео |
| Батерия | технология : литиево-йонна |
|  | живот : до 4 ч. и 30 мин. |

| Таблет | 6 броя |
| --- | --- |
| Процесор | NVIDIA Tegra 3 - 1.3 GHz (Четириядрен) |
| Системна памет | 1GB RAM |
| Памет | 16GB |
| Дисплей | 7-инчов (1280x800) HD дисплей, IPS панел с подсветка и устойчиво на надраскване стъкло |
| Функционалност | micro USB порт |
|  | 3.5 мм аудио жак |
|  | вграден микрофон |
|  | вградени говорители |
|  | акселерометър |
|  | GPS |
|  | Магнитометър |
|  | Жироскоп |
|  | NFC |
| Операционна система | Android 4.1 (Jelly Bean) |
| Камера | 1.2-мегапикселова в предната част |
| Свързаност | Bluetooth 3.0, WiFi 802.11 b/g/n, GPS |
| Тегло | 340 грама |
| Батерия | 4325 mAh (9 часа HD видеовъзпроизвеждане, 10 часа сърфиране в интернет, 10 часа четене на електронни книги и 300 часа в режим на готовност) |

| Компютърна конфигурация 1 | 1 брой |
| --- | --- |
| Mainboard |  |
| Chipset | Intel® Z77 Express Chipset |
| Onboard Graphics | Integrated Graphics Processor: |
|  | 1 x D-Sub port |
|  | 1 x DVI-D port, supporting a maximum resolution of 1920x1200 |
|  | 1 x HDMI port, supporting a maximum resolution of 1920x1200 |
| Audio | VIA VT2021 codec High Definition Audio 2/4/5.1/7.1-channel Support for S/PDIF Out |
| LAN | Atheros GbE LAN chip (10/100/1000 Mbit) |
| Expansion Slots | 1 x PCI Express x16 slot, running at x16 (PCIEX16) (The PCIEX16 slot conforms to PCI Express 3.0 standard.) 1 x PCI Express x16 slot, running at x4 (PCIEX4) 1 x PCI Express x1 slot (The PCIEX4 and PCIEX1 slots conform to PCI Express 2.0 standard.) 1 x PCI slot |
| Multy-Graphics Technology | Support for AMD CrossFireX™ technology |
| Storage Interface | 2 x SATA 6Gb/s connectors (SATA3 0/1) supporting up to 2 SATA 6Gb/s devices 4 x SATA 3Gb/s connectors (SATA2 2/3/4/5) supporting up to 4 SATA 3Gb/s devices Support for RAID 0, RAID 1, RAID 5, and RAID 10 |
| USB | Up to 10 USB 2.0/1.1 ports (4 ports on the back panel, 6 ports available through the internal USB headers) Up to 4 USB 3.0/2.0 ports (2 ports on the back panel, 2 ports available through the internal USB headers) |
| Internal I/O Connectors | 1. 1 x 24-pin ATX main power connector |
|  | 2. 1 x 8-pin ATX 12V power connector |
|  | 3. 2 x SATA 6Gb/s connectors |
|  | 4. 4 x SATA 3Gb/s connectors |
|  | 5. 1 x CPU fan header |
|  | 6. 2 x system fan headers |
|  | 7. 1 x front panel header |
|  | 8. 1 x front panel audio header |
|  | 9. 1 x S/PDIF Out header |
|  | 10. 1 x USB 3.0/2.0 header |
|  | 11. 3 x USB 2.0/1.1 headers |
|  | 12. 1 x serial port header |
|  | 13. 1 x parallel port |
|  | 14. 1 x Trusted Platform Module (TPM) header |
|  | 15. 1 x Clear CMOS jumper |
| Back Panel Connectors | 1. 1 x PS/2 keyboard/mouse port |
|  | 2. 1 x D-Sub port |
|  | 3. 1 x DVI-D port |
|  | 4. 1 x HDMI port |
|  | 5. 2 x USB 3.0/2.0 ports |
|  | 6. 4 x USB 2.0/1.1 ports |
|  | 7. 1 x RJ-45 port |
|  | 8. 3 x audio jacks (Line In/Line Out/Microphone) |
| I/O Controller | 1. iTE I/O Controller Chip |
| H/W Monitoring | 1. System voltage detection |
|  | 2. CPU/System temperature detection |
|  | 3. CPU/System fan speed detection |
|  | 4. CPU overheating warning |
|  | 5. CPU/System fan fail warning |
|  | 6. CPU/System fan speed control |
| BIOS | 1. 2 x 64 Mbit flash |
|  | 2. Use of licensed AMI EFI BIOS |
|  | 3. PnP 1.0a, DMI 2.0, SM BIOS 2.6, ACPI 2.0a |
| Form Factor | 1. Micro ATX Form Factor; 24.4cm x 22.0cm |
| Processor |  |
| # of Cores | 4 |
| # of Threads | 4 |
| Clock Speed | 3.4 GHz |
| Max Turbo Frequency | 3.8 GHz |
| Intel® Smart Cache | 6 MB |
| Bus/Core Ratio | 34 |
| DMI | 5 GT/s |
| Instruction Set | 64-bit |
| Instruction Set Extensions | SSE4.1/4.2, AVX |
| Embedded Options Available | No |
| Lithography | 22 nm |
| Max TDP | 77 W |
| Memory Specifications |  |
| Max Memory Size (dependent on memory type) | 32 GB |
| Memory Types | DDR3-1333/1600 |
| # of Memory Channels | 2 |
| Max Memory Bandwidth | 25.6 GB/s |
| ECC Memory Supported | No |
| Graphics Specifications |  |
| Processor Graphics | HD Graphics 2500 |
| Graphics Base Frequency | 650 MHz |
| Graphics Max Dynamic Frequency | 1.15 GHz |
| # of Displays Supported | 3 |
| Expansion Options |  |
| PCI Express Revision | 3.0 |
| PCI Express Configurations | 1x16, 2x8, 1x8 & 2x4 |
| Package Specifications |  |
| Max CPU Configuration | 1 |
| TCASE | 67.4°C |
| AES New Instructions | Yes |
| RAM | 8 GB DDR3 1600 MHz 240 Pin Unbuffered DIMM (2 броя x 4 GB) |
| Suitable for | Desktop PC |
| Module Specification | 240Pin Unbuffered DIMM |
| Density | 1GB/2GB/4GB/8G |
| IC Configuration | 128 x 8, 256 x 8, 512x8 |
| CAS Latency | 11-11-11-28 |
| Working Voltage | 1.5V |
| HDD | 2TB 7200 64MB SATA III |
| Form Factor | 3.5" |
| Interface Options | SATA 6Gb/s |
| Performance |  |
| Spindle Speed (RPM) | 7 000 |
| Cache (MB) | 4 |
| Transfer Rate, Max Ext (MB/s) | 600 |
| Sustained Data Rate OD | 210MB/s |
| Average Latency (ms) | 4.16 |
| Reliability/Data Integrity |  |
| Nonrecoverable Read Errors per Bits Read | 1 in 1014 |
| Annualized Failure Rate (AFR) | <1% |
| Power Management |  |
| Idle, Typical Operating (W) | 4.6 |
| Shock |  |
| Operating: Gs (ms) | 80 (2ms) |
| Non-operating: Gs (ms) | 300 (2ms) |
| Acoustics (bels - sound power) |  |
| HDD | 64 GB SSD |
| Capacity | 32GB / 64GB |
| NAND Flash | Multi-Level Cell (MLC) Synchronous NAND Flash Memory |
| Interface | SATA 3Gb/s |
| Form Factor | 2.5 inch |
| Performance | 32GB Performance (ATTO) : |
|  | Read: Up to 280MB/s |
|  | Write: Up to 260MB/s |
|  | Multimedia Data Transfer (AS-SSD) |
|  | MAX 4K write IOPS up to 40K |
| Shock Resistance | 1500G |
| MTBF | 1,000,000 hrs |
| DVD RW | DVD записващо/четящо устройство |
| SVGA Card |  |
| Gpu cores | 1280 stream processors |
| Core Clock | 900 MHz |
| Digital max resolution | 2560 x 1600 |
| Analog max resolution | 2048 x 1536 |
| Process Technology | 28 nm |
| PCB Form | ATX |
| Memory Clock | 4800 MHz |
| Memory Size | 1 GB |
| Memory Bus | 256 bit |
| Card Bus | PCI-E 3.0 |
| Memory Type | GDDR5 |
| DirectX | 11 |
| OpenGL | 4.2 |
| Multi-view | 4 |
| I/O | HDMI * 1 |
|  | DVI-I * 1 |
|  | Mini DisplayPort * 2 |
| Card size | H= 42.5mm, L=241 mm, W= 137mm |
| Power requirement | 500 W |
| Monitor |  |
| Screen size (inches) | 23 |
| Panel Type (TN, IPS) | IPS |
| Aspect Ratio | 16:09 |
| Resolution | 1920 x 1080 |
| Brightness (cd/m2) | 250 |
| Contrast Ratio | 5000000:1 |
| Response Time (ms) | 5 |
| Viewing Angle (°) | 178 /178 (CR≥10) |
| Colour Depth (Num of Colours) | 16.7M |
| Surface Treatment | Anti-Glare,3H |
| Input / Output |  |
| D-Sub | Yes |
| DVI-D | Yes |
| HDMI | Yes |
| Headphone Out | Yes |
| Features |  |
| sRGB | Yes |
| DDC/CI | Yes |
| HDCP | Yes |
| Intelligent Auto | Yes |
| Plug & Play | Yes |
| Forte Pivot | Yes |
| Color |  |
| Stand |  |
| Base detachable | Yes |
| Tilt(Angle) | Yes / -5º(+/-3°）(front) ~ 20º(+/-3°）(rear) |
| STANDARD (CERTIFICATION) & VESA MOUNTING |  |
| TCO5.2 | Yes |
| UL(cUL) | Yes |
| TUV-GS | TUV-Type |
| FCC-B, CE | Yes |
| Case & PSU | АТХ кутия + Compaq 550w |
| Color | White/Black |
| Keyboard | Да |
| Mouse | Да |

| Компютърна конфигурация 2 | 31 броя |
| --- | --- |
| Дънна платка |  |
| Chipset | Intel® H61(B3) |
| Memory | 2 x DIMM, Max. 16GB, DDR3 1333/1066 MHz Non-ECC, Un-buffered Memory |
|  | Dual Channel Memory Architecture |
| Graphic | Integrated Graphics Processor |
|  | Multi-VGA output support : HDMI/DVI/RGB ports |
|  | Supports DirectX 10.1 |
| Expansion Slots | 1 x PCIe 2.0 x16 |
|  | 2 x PCIe 2.0 x1 |
|  | 1 x PCI |
| Storage | 4 x SATA 3Gb/s port(s |
| LAN | Realtek®, 1 x Gigabit LAN Controller(s) |
| Audio | Realtek® ALC887 8-Channel High Definition Audio CODEC *1 |
|  | - Supports : Jack-detection, Front Panel Jack-retasking |
| USB Ports | Built-in Controller : |
|  | 10 x USB 2.0 port(s) (6 at back panel, black, 4 at mid-board) |
| Special Features | 100% All High-quality Conductive Polymer Capacitors |
| Back I/O Ports | 1 x PS/2 keyboard/mouse combo port(s) |
|  | 1 x DVI |
|  | 1 x D-Sub |
|  | 1 x HDMI |
|  | 1 x LAN (RJ45) port(s) |
|  | 6 x USB 2.0 |
|  | 1 x Optical S/PDIF out |
|  | 3 x Audio jack(s) |
| Internal I/O Ports | 2 x USB 2.0 connector(s) support(s) additional 4 USB 2.0 port(s) |
|  | 1 x COM port(s) connector(s) |
|  | 4 x SATA 3Gb/s connector(s) |
|  | 1 x CPU Fan connector(s) |
|  | 1 x Chassis Fan connector(s) |
|  | 1 x S/PDIF out header(s) |
|  | 1 x 24-pin EATX Power connector(s) |
|  | 1 x 4-pin ATX 12V Power connector(s) |
|  | 1 x parallel port connector(s) |
|  | 1 x Front panel audio connector(s) (AAFP) |
|  | 1 x System panel(s) |
| BIOS | 32 Mb Flash ROM , EFI AMI BIOS, PnP, DMI2.0, WfM2.0, ACPI v2.0a, SM BIOS v2.6, Multi-language BIOS |
| Form Factor | uATX Form Factor |
| Processor |  |
| # of Cores | 4 |
| # of Threads | 4 |
| Clock Speed | 3 GHz |
| Max Turbo Frequency | 3.3 GHz |
| Intel® Smart Cache | 6 MB |
| Bus/Core Ratio | 30 |
| DMI | 5 GT/s |
| Instruction Set | 64-bit |
| Instruction Set Extensions | SSE4.1/4.2, AVX |
| Lithography | 32 nm |
| Max TDP | 95 W |
| Memory Types | DDR3-1066/1333 |
| # of Memory Channels | 2 |
| Max Memory Bandwidth | 21 GB/s |
| ECC Memory Supported | No |
| Processor Graphics |  |
| Graphics Base Frequency | 850 MHz |
| Graphics Max Dynamic Frequency | 1.1 GHz |
| Dual Display Capable | Yes |
| # of Displays Supported | 2 |
| PCI Express Revision | 2.0 |
| # of PCI Express Lanes | 16 |
| Max CPU Configuration | 1 |
| Sockets Supported | LGA1155 |
| AES New Instructions | Yes |
| Idle States | Yes |
| Thermal Monitoring Technologies | Yes |
| Execute Disable Bit | Yes |
| RAM | 8GB DDR3 1333MHz |
| HDD |  |
| Interface | SATA 3Gb/s |
| Capacity (GB) | 1TB/750/640/500/320/250/160 |
| Max areal density (Gbits/sq. in.) | 352 |
| Data buffer (MB) | 32/32/32/16/16/8/8 |
| Rotational Speed (RPM) | 7,2 |
| Media transfer rate (Mbits/sec, max) | 1589 |
| Interface transfer rate (MB/sec, max) | 300 |
| Error Rate (non-recoverable, bits read) | 1 in 10^14 |
| Load/Unload Cycles | 300 |
| Idle (Bels) | 2.4 (1TB/750GB/640GB) |
|  | 2.5 (500GB/320GB/250GB/160GB) |
| Requirement | +5 VDC (+/-5%) |
|  | +12 VDC (+/-10%) |
| Requirement: Start-up (W, peak, max) | 1.5 (+5V), 2.0 (+12V) |
| Monitor |  |
| Screen Size | 21.5" (16:9) |
| Brightness | 200cd/m² |
| Contrast Ratio | DCR 5,000,000:1 (Static: 600:1) |
| Resolution | 5,000,000:1 |
| Response Time | 1920 x 1080 |
| Viewing Angle (Horizontal/Vertical) | R/L: 45/45 (Typ), U/D: 20/45 (Tpy) |
| Colour Support | 16.7M |
| Video Signal | D-sub |
| Sync. Signal | Separate, Composite, SOG |
| Connector | D-sub |
| Power Consumption | 28W |
| Stand-by Power (DPMS) | 0.3W (Typical) |
| Type | Extend Adaptor |
| Plug&Play | DDC 2B |
| Energy/Environment Mark | Energy Star |
| Cabinet Colour | High Glossy Black |
| Stand Function | Tilt |
| Optical drive | DVD записващо/четящо устройство |
| Interface Type | SATA |
| GPU |  |
| Bus Standard | PCI Express 2.0 |
| Video Memory | GDDR5 |
| Engine Clock | 910 MHz |
| CUDA Core | 192 |
| Shader Clock | 1800 MHz |
| Memory Clock | 4104 MHz ( 1026 MHz GDDR5 ) |
| Memory Interface | 192-bit |
| Resolution | D-Sub Max Resolution : 2048x1536 |
|  | DVI Max Resolution : 2560x1600 |
| Interface | D-Sub Output : Yes x 1 |
|  | DVI Output : Yes x 1 |
|  | HDMI Output : Yes x 1 |
|  | HDCP Support : Yes |
| Power Consumption | up to 150W(1 additional 6 pin PCIe power required) |
| Слушалки | Стерео слушалки |
| Мишка и клавиатура | да |
| Кутия | ATX 500W |

| Компютърна конфигурация 3 | 58 броя |
| --- | --- |
| Mainboard |  |
| Chipset | 1. AMD A85X |
| Memory | 1. 4 x 1.5V DDR3 DIMM sockets supporting up to 64 GB of system memory |
|  | 2. Dual channel memory architecture |
|  | 3. Support for DDR3 1866/1600/1333/1066 MHz memory modules |
|  | 4. Support for AMD Memory Profile (AMP)/ Extreme Memory Profile (XMP) memory modules |
| Onboard Graphics | APU: |
|  | 1. 1 x D-Sub port |
|  | 2. 1 x DVI-D port, supporting a maximum resolution of 2560x1600 |
|  | 3. 1 x HDMI port, supporting a maximum resolution of 1920x1200 |
|  | 4. 1 x DisplayPort, supporting a maximum resolution of 2560x1600 |
| Audio | 1. Realtek ALC892 codec |
|  | 2. High Definition Audio |
|  | 3. 2/4/5.1/7.1-channel |
|  | 4. Support for S/PDIF Out |
| LAN | 1. Realtek GbE LAN chip (10/100/1000 Mbit) |
| Expansion Slots | 1. 1 x PCI Express x16 slot, running at x16 (PCIEX16) |
|  | 2. 1 x PCI Express x16 slot, running at x8 (PCIEX8) |
|  | 3. 1 x PCI Express x16 slot, running at x4 (PCIEX4) |
|  | 4. 3 x PCI Express x1 slots |
|  | (All PCI Express slots conform to PCI Express 2.0 standard.)  |
|  | 5. 1 x PCI slot |
| Multi-Graphics Technology | 1. Support for AMD CrossFire™ technology |
|  | 2. Support for AMD Dual Graphics technology |
| Storage Interface | Chipset: |
|  | 1. 7 x SATA 6Gb/s connectors (SATA3 0~6) supporting up to 7 SATA 6Gb/s devices |
|  | 2. 1 x eSATA 6Gb/s connector on the back panel supporting up to 1 SATA 6Gb/s device |
|  | 3. Support for RAID 0, RAID 1, RAID 5, RAID 10, and JBOD |
| USB | Chipset: |
|  | 1. Up to 4 USB 3.0/2.0 ports (2 ports on the back panel, 2 ports available through the internal USB header) |
|  | 2. Up to 10 USB 2.0/1.1 ports (2 ports on the back panel, 8 ports available through the internal USB headers) |
|  | Etron EJ168 chip: |
|  | 1. Up to 2 USB 3.0/2.0 ports on the back panel |
| Internal I/O Connectors | 1. 1 x 24-pin ATX main power connector |
|  | 2. 1 x 8-pin ATX 12V power connector |
|  | 3. 7 x SATA 6Gb/s connectors |
|  | 4. 4 x system fan headers |
|  | 5. 1 x front panel header |
|  | 6. 1 x front panel audio header |
|  | 7. 1 x S/PDIF Out header |
|  | 8. 1 x USB 3.0/2.0 header |
|  | 9. 4 x USB 2.0/1.1 headers |
|  | 10. 1 x Clear CMOS jumper |
|  | 11. 1 x Trusted Platform Module (TPM) header |
|  | 12. 1 x Clear CMOS button |
| Back Panel Connectors | 1. 1 x PS/2 keyboard/mouse port |
|  | 2. 1 x D-Sub port |
|  | 3. 1 x DVI-D port |
|  | 4. 1 x optical S/PDIF Out connector |
|  | 5. 1 x HDMI port |
|  | 6. 1 x DisplayPort |
|  | 7. 4 x USB 3.0/2.0 ports |
|  | 8. 2 x USB 2.0/1.1 ports |
|  | 9. 1 x eSATA 6Gb/s connector |
|  | 10. 1 x RJ-45 port |
|  | 11. 6 x audio jacks (Center/Subwoofer Speaker Out/Rear Speaker Out/Side Speaker Out/Line In/Line Out/Microphone) |
| I/O Controller | 1. iTE I/O Controller Chip |
| H/W Monitoring | 1. System voltage detection |
|  | 2. APU/System temperature detection |
|  | 3. APU/System fan speed detection/ control |
|  | 4. APU overheating warning |
|  | 5. APU/System fan fail warning |
| BIOS | 1. 2 x 64 Mbit flash |
|  | 2. Use of licensed AMI EFI BIOS |
|  | 3. PnP 1.0a, DMI 2.0, SM BIOS 2.6, ACPI 2.0a |
| Form Factor | 1. ATX Form Factor; 30.5cm x 24.4cm |
| CPU |  |
| CPU Clock Speed | 4.2GHz |
|  | 3.8GHz |
| CPU Cores on Die | 4 cores |
| TDP | 100W |
| Total L2 Cache | 4MB |
| Radeon™Cores on Die | 384 |
| GPU Clock Speed | 800 MHz |
| DIRECTX® Version | 11 |
| UVD | UVD3.2 |
| DDR3 Speed | 1866 |
| RAM | 2 x 4GB ADATA DDR III 1600 |
| Module Specification | 240Pin Unbuffered DIMM |
| Density | 4GB |
| CAS Latency | 11 |
| Working Voltage | 1.5V ± 0.075V |
| HDD | 1TB |
| Form Factor | 3.5" |
| Interface Options | SATA 6Gb/s |
| Spindle Speed (RPM) | 7200 |
| Cache (MB) | 64 |
| Transfer Rate, Max Ext (MB/s) | 600 |
| Sustained Data Rate OD | 210MB/s |
| Average Latency (ms) | 4.16 |
| Non-recoverable Read Errors per Bits Read | 1 in 1014 |
| Annualized Failure Rate (AFR) | <1% |
| Monitor |  |
| Monitor Panel Type | TFT-LCD |
| Backlight | LED |
| Panel Size | 23.6" W (59.9 cm) |
| Aspect Ratio | 16:09 |
| Brightness | 250 cd/m² |
| SmartContrast | 20,000,000:1 |
| Contrast Ratio (typ.) | 1000:01:00 |
| Response Time (typ.) | 5ms |
| SmartResponse | 2ms |
| Optimum Resolution | 1920x1080@60Hz |
| Viewing Angle | 170° (H) / 160° (V) @ C/R > 10 |
|  | 178° (H) / 170° (V) @ C/R > 5 |
| Display Colors | 16.7M |
| Vertical Refresh Rate | 56Hz - 76Hz |
| Horizontal Frequency | 30kHz - 83kHz |
| sRGB | YES |
| Connectivity |  |
| Signal Input | DVI (Digital), VGA (Analog), |
|  | HDMI (available for model 247E3LH, 247E3LPH) |
| Stand | Tilt -5 / +20 |
| Кутия | ATX 400W |
| Клавиатура | Да |
| Мишка | Да |

| Компютърна конфигурация 4 | 39 броя |
| --- | --- |
| Mainboard |  |
| Chipset | 1. Intel® H61 Express Chipset |
| Memory | 1. 2 x 1.5V DDR3 DIMM sockets supporting up to 16 GB of system memory |
|  | 2. Dual channel memory architecture |
|  | 3. Support for DDR3 1333/1066/800 MHz memory modules |
|  | 4. Support for non-ECC memory modules |
|  | 5. Support for Extreme Memory Profile (XMP) memory modules |
| Onboard Graphics | Integrated Graphics Processor: |
|  | 1. 1 x D-Sub port |
| Audio | 1. Realtek ALC887 codec |
|  | 2. High Definition Audio |
| LAN | Realtek GbE LAN chip (10/100/1000 Mbit) |
| Expansion Slots | 1 x PCI Express x16 slot, running at x16 |
|  | (The PCI Express x16 slot conforms to PCI Express 3.0 standard.) |
|  | 2. 2 x PCI Express x1 slots |
|  | (All PCI Express x1 slots conform to PCI Express 2.0 standard.) |
| Storage Interface | 4 x SATA 3Gb/s connectors supporting up to 4 SATA 3Gb/s devices |
| USB | Up to 8 USB 2.0/1.1 ports (4 ports on the back panel, 4 ports available through the internal USB headers) |
| Internal I/O Connectors | 1. 1 x 24-pin ATX main power connector |
|  | 2. 1 x 4-pin ATX 12V power connector |
|  | 3. 4 x SATA 3Gb/s connectors |
|  | 4. 1 x CPU fan header |
|  | 5. 1 x system fan header |
|  | 6. 1 x front panel header |
|  | 7. 1 x front panel audio header |
|  | 8. 2 x USB 2.0/1.1 headers |
|  | 9. 1 x Clear CMOS jumper |
| Back Panel Connectors | 1. 1 x PS/2 keyboard port |
|  | 2. 1 x PS/2 mouse port |
|  | 3. 1 x D-Sub port |
|  | 4. 1 x serial port header |
|  | 5. 1 x parallel port |
|  | 6. 4 x USB 2.0/1.1 ports |
|  | 7. 1 x RJ-45 port |
|  | 8. 3 x audio jacks (Line In/Line Out/Microphone) |
| I/O Controller | 1. iTE I/O Controller Chip |
| H/W Monitoring | 1. System voltage detection |
|  | 2. CPU/System temperature detection |
|  | 3. CPU/System fan speed detection / control |
| BIOS | 1. 2 x 32 Mbit flash |
|  | 2. PnP 1.0a, DMI 2.0, SM BIOS 2.6, ACPI 2.0a |
| Form Factor | 1. Micro ATX Form Factor; 22.6cm x 17.4cm |
| Processor |  |
| # of Cores | 2 |
| # of Threads | 2 |
| Clock Speed | 2.7 GHz |
| Intel® Smart Cache | 3 MB |
| Bus/Core Ratio | 27 |
| DMI | 5 GT/s |
| Instruction Set | 64-bit |
| Instruction Set Extensions | SSE4.1/4.2 |
| Lithography | 32 nm |
| Max TDP | 65 W |
| Memory Types | DDR3-1066 |
| # of Memory Channels | 2 |
| Max Memory Bandwidth | 17 GB/s |
| Processor Graphics |  |
| Graphics Base Frequency | 850 MHz |
| Graphics Max Dynamic Frequency | 1.1 GHz |
| Dual Display Capable | Yes |
| # of Displays Supported | 2 |
| Expansion Options |  |
| PCI Express Revision | 2.0 |
| Max CPU Configuration | 1 |
| Sockets Supported | FCLGA1155 |
| Low Halogen Options Available | See MDDS |
| RAM | 4 GB DDR3 1333 A-Data 240 Pin Unbuffered DIMM |
| Suitable for | Desktop PC |
| Module Specification | 240Pin Unbuffered DIMM |
| Density | 1GB/2GB/4GB/8G |
| IC Configuration | 128 x 8, 256 x 8, 512x8 |
| CAS Latency | 9 |
| Working Voltage | 1.5V ± 0.075V |
| HDD |  |
| Form Factor | 3.5" |
| Interface Options | SATA 6Gb/s |
| Performance |  |
| Spindle Speed (RPM) | 7200 |
| Cache (MB) | 16 |
| Transfer Rate, Max Ext (MB/s) | 600 |
| Sustained Data Rate OD | 125MB/s |
| Average Latency (ms) | 4.16 |
| Reliability/Data Integrity |  |
| Nonrecoverable Read Errors per Bits Read | 1 in 1014 |
| Annualized Failure Rate (AFR) | <1% |
| Power Management |  |
| Idle, Typical Operating (W) | 4.6 |
| Temperature |  |
| Operating | 0° to 60°C |
| Non-operating | -40° to 70°C |
| Shock |  |
| Operating: Gs (ms) | 70 (2ms) |
| Non-operating: Gs (ms) | 350 (2ms) |
| Monitor |  |
| Product Color | Glossy Black |
| Screen Size | 18.5”W |
| Aspect Ratio | 16:09 |
| Resolution (max.) | 1366x768 |
| Pixel Pitch (mm) | 0.3 |
| Brightness ( typ.) | 200 cd/m2 |
| Native Contrast ( typ. ) | 700:01:00 |
| DCR (Dynamic Contrast Ratio) | 50000:1 |
| Panel Type | TN |
| Viewing Angle (L/R;U/D) (CR>=10) | 90/65 |
| Response Time(Tr+Tf) typ. | 5ms |
| Display Colors | 16.7million |
| Color Gamut | 68% |
| Input Connector | D-sub |
| Power |  |
| Power Supply (90~264 AC) | Built-in |
| Power Consumption (On mode) | 24W (max.) |
| (Power saving mode) | <0.3W |
| HDCP | No |
| Color Temperature | Reddish / Normal/ Bluish /User mode |
| VESA Wall Mounting | 100x100mm |
| Case & PSU | ATX 400W |
| Keyboard | Да |
| Mouse | Да |

| Монитор | 3 броя |
| --- | --- |
| Цвят | Glossy Black |
| Размер | 18.5”W |
| Аспектно съотношение | 16:9 |
| Резолюция | 1366x768 |
| Яркост | 200 cd/m2 |
| Контраст | 700:01:00 |
| Динамичен контраст) | 50000:1 |
| Време на реакция(Tr+Tf) typ. | 5ms |
| Вход | D-sub |
| Захранване (90~264 AC) | Built-in |
| Косумация | 24W (max.) |

| Екран за презентации | 2 броя |
| --- | --- |
| Размер | 70.3 x 58.1 x 2.7" (178.6 x 147.6 x 6.9 cm) |
| Аспектно съотношение | 4:3 |

| Диктофон | 3 броя |
| --- | --- |
| Свързване с компютър | Да |
| Формат на запис | Линейно PCM/MP3 |
| Вход за микрофон | Да |
| Вграден микрофон | Стерео (S-Mic) |
| Елиминиране на шума | Да (интелигентно елиминиране на шума) |
| Възпроизвеждане при | Да |
| Стерео слушалки | Да |
| Вградена памет | 4 GB |
| Жак за слушалки | Да |
| Тип батерии | ААА х 1 |
| Формат на възпроизвеждане | MP3/AAC/WMA/WAV |
| USB порт | Да (директно) |
| Слот за карта с памет | MicroSD/M2 |
| Scene Select | Да |
| Нискосрязващ филтър | Да |
| VOR | Да |
| Функция синхронизиран запис | Да |
| Дисплей на записа | Да |
| Цифрово регулиране на височината на звука (DPC) (управление на скоростта) | Да |
| Графичен еквалайзер | Да |
| Повторение A-B | Да |
| Маркер на песен | Да |
| Изтриване | Да |
| Защита | Да |
| Разделяне | Да |
| Преместване на файл | Да |
| Копиране на файл | Да |
| LCD осветяване отзад | Да |
| Зареждане чрез USB връзка | Да |
| Калъф за носене | Да |
| Батерия | Акумулаторна батерия (NiMH, размер ААА) x 1 |

| Безжично устройство | 6 броя |
| --- | --- |
| компонент | описание | брой |
| Дънна платка | Mikrotik RB435G | 1 |
| WiFi Карта | R52hN | 2 |
| Pigtail |  | 2 |
| Кутия |  | 1 |
| Антена | Omni (1 x 2,5GHz и 1 x 5GHz) | 2 |
| Захранване |  | 1 |

| Безжично устройство RB2011UAS-2HnD-IN | 2 броя |
| --- | --- |

| Дисков масив QSAN P400Q-S424 6x 1G iSCSI Single Upgradeable | 2 броя |
| --- | --- |
| RAID Controller | Single Upgradeable to Dual |
| No. of Host Channels Per Controlle | 6 x 1GbE iSCSI |
| Expansion Enclosure | 300Q series |
| Cache Memory Per Controller | 4GB, up to 8GB |
| No. of Hard Drives (SAS & SATA II) | 24 |
| Max. No. of Hard Drives (SAS & SATA II) | 192 |
| Power Supply | 3 x 500W |
| Fan | 2 |
| Dimensions | 4U 19” Rackmount |
| Feature Highlights |  |
| SCSI Hardware | iSCSI off-load engine |
|  | iSCSI jumbo frame |
| RAID & Volume RAID level | 0,1,0+1,3,5,6,10,30,50,60 |
|  | Up to 4096 logical volumes |
| Global and dedicated hot spare | Yes |
| Online volume expansion and migration | Yes |
| Auto volume rebuilding | Yes |
| High Availability Dual-active RAID controller | Yes |
| QSnap writable snapshots | Yes |
| Multi-path & load-balancing support | Microsoft MPIO |
|  | MC/S |
|  | Trunking |

| Твърд диск | 48 броя |
| --- | --- |
| Hard Drive Model | Western Digital 2000GB SATA II RE4 64MB |
| Interface | SATA 3 Gb/s |
| Capacity | 2000 GB |
| Buffer Size | 64 MB |

| Мрежов рутер | 1 брой |
| --- | --- |
| Mikrotik AH1100 |  |

| Комутатор | 4 броя |
| --- | --- |
| Ports | 24 х 10/100/1000BASE-T PoE |
|  | 4 х combo 10/100/1000BASE-T/SFP |
| Switch Capacity | 48Gbps |
| Packet Fowarding Rate | 35.7Mpps |
| MAC Address Table Size | 8K |
| MAC Address Update | Up to 256 static MAC entries |
|  | Enable/disable auto-learning of MAC addresses |
| Packet Buffer | 512KB |
| Jumbo Frame | 10,240 Bytes |
| Power Input | 102 to 240 VAC |
|  | 50/60Hz internal universal power supply |
| PoE Budget | 180 watts |
| DC Fans | 2 |
| Heat Dissipation | 854.02BTU/hr |
| Acoustic Value | 47 dB |
| Dimensions | 440mm x 210mm x 44mm |
| Size | 19-inch standard rackmounting width |
|  | 1U height |
| Weight | 3.6 kg |
| EMI | FCC Class A |
|  | CE Class A |
|  | VCCI Class A |
| Safety | cUL |
|  | LVD |

Забележка: Да се предлагат  офертите по обособените позиции

# Comments

BenQ MS502

MMP1011

BenQ MX503

Nec M260WSG

TRIUMPH BOARD 96” DUAL Touch USB with SW

# TRIUMPH BOARD DUAL TOUCH

HP Scanjet G3110 Photo Scanner

Xerox Phaser 3010

HP LaserJet Pro 400 M401dn

Samsung NP300E5X

Toshiba Satelite C855-149

Asus Google Nexus 7

GigaByte Z77M-D3H

Intel® Core™ i5-3570 Processor

SEAGATE  2TB  7200 64MB SATA III

A-Data 64 GB Premier SP800 SSD

GV-R785OC-1GD

LG 23" IPS234V-PN

Asus P8H61-M

i5-2320

Deskstar 7K1000.C HDS721010CLA332

Samsung S22A100N

Asus ENGTX550 Ti

Gigabyte GA-F2A85X-UP4 FM2

AMD A10-5800 X4 Quad Core

Seagate 1000GB 7200 64MB SATA III

PHILIPS 23.6” 247E3LSU

GA-H61M-DS2(rev. 3.0)

Intel® Pentium® Processor G630 (3M Cache, 2.70 GHz)

SEAGATE 500GB 7200 16MB SATA III

BENQ 18.5" G950A, 5ms, 50000:1, 200cd/m2

BENQ	18.5" G950A

Sony ICD-UX513F/W

Dlink DGS-1210-28P 24 Port Gigabit Web Smart Poe